## Slide 1: CSED311 Lab1: ALU
Sanghwan Jang
jsh710101@postech.ac.kr

## Slide 2: Contents
Team Announcement
Assignment Announcement
Report & Demo

## Slide 3: Team Announcement
1 | 손주은 | 정준혁
2 | 김수창 | 조상혁
3 | 박수완 | 이준호
4 | 이승준 | 김윤수
5 | 김병수 | 문민재
6 | 박지훈 | 
7 | 민유영 | 김성남
8 | 최지훈 | 이준석
9 | 홍윤재 | 김동현
10 | 최진환 | 강혁규
11 | 홍승하 | 조현욱
12 | 석민상 | 박건우
13 | 류나현 | 주광진
14 | 송시호 | 김승현
15 | 장영상 | 전현
16 | 형은영 | 엄태강
17 | 강다현 | 이다영
18 | 제상은 | 
19 | 김정우 | 정성윤
20 | 이재엽 | 
21 | 곽성재 | 
22 | 정윤우 | 유태형
23 | 이정우 | 권동현
24 | 명성현 | 조승혁
25 | 박재준 | 김승진
26 | 정채윤 | 문새미
27 | 김진수 | 
28 | 강민수 | 김동현
29 | 박민준 | 조채은
30 | 이재원 | 
31 | 김민성 | 이창훈
32 |  | 
33 |  | 
34 |  | 
35 |  | 
강다현 강민수 강혁규 곽성재 권동현 김동현 김동현 김민성 김병수 김성남 김성태 김수창 김승진 김승현 김윤수 김정우 김종민 김진수 김호영 류나현 명성현 문민재 문새미 민유영 박건우 박민준 박수완 박재준 박지훈 석민상 손주은 송시호 엄태강 유태형 이다영 이서림 이승준 이재엽 이재원 이정우 이정은 이준석 이준호 이창훈 장영상 전현 정성윤 정윤우 정준혁 정채윤 제상은 조상혁 조승혁 조채은 조현욱 주광진 최지훈 최진환 편현장 형은영 홍승하 홍윤재

## Slide 4: Assignment Announcement
Implement ALU (Arithmetic Logic Unit) in Verilog
  Input: (A, B, FuncCode)
    A: left operand (16-bit signed binary)
    B: right operand (16-bit signed binary)
    FuncCode: operator (4-bit binary)
  Output: (C, OverflowFlag)
    C: operation result (16-bit signed binary)
    OverflowFlag: overflow flag (1-bit binary)
Submit report and code to LMS
  Due date: 2019. 3. 5 6:30 pm
  We will check the demo in the next Lab session.

## Slide 5: Assignment Announcement
FuncCode | Operation | Comment
0000 | A + B | Signed addition
0001 | A - B | Signed subtraction
0010 | A | Identity
0011 | ~A | Bitwise not
0100 | A & B | Bitwise and
0101 | A ¦ B | Bitwise or
0110 | A nand B | Bitwise nand
0111 | A nor B | Bitwise nor
ALU Specification
FuncCode | Operation | Comment
1000 | A xor B | Bitwise xor
1001 | A xnor B | Bitwise xnor
1010 | A << 1 | Logical left shift
1011 | A >> 1 | Logical right shift
1100 | A <<< 1 | Arithmetic left shift
1101 | A >>> 1 | Arithmetic right shift
1110 | ~A + 1 | Two’s complement
1111 | 0 | Zero

## Slide 6: Assignment Announcement
Overflow Detection
  For addition and subtraction, You should detect overflow (and set the flag).
  For other operations, OverflowFlag is always zero.
OverflowFlag | Signed addition | Signed subtraction
0 | Result is correct | Result is correct
1 | Result is incorrect | Result is incorrect

## Slide 7: Assignment Announcement
Submission
  Submit your assignment to LMS in a single zip file with filename:
    Lab1_StudentID.zip
  This zip file should contain:
    Lab1_StudentID_Report.pdf
      PDF file of your report
    Lab1_StudentID_Code.zip
      Zip file of your code (*.v)

## Slide 8: Report
Submit as a PDF file
  Lab1_StudentID_Report.pdf
You can use Korean or English to write your report.
READABILITY !!
  Please help TAs to read it.
  I encourage you to write a simple and clear report.
  The length of the report is not related to the score.

## Slide 9: Report
I encourage you to write the 5 sections as follows.
  Introduction
  Design
  Implementation
  Discussion
  Conclusion
Other formats are OK if your report contains all the required content.

## Slide 10: Report
Introduction
  You should describe:
    What you have to design & implement
    What you have to learn
Design
  You can save a lot of time with a careful design!
  You should make an effort to write this section. For example:
    How to divide a large module into submodules?
    How does each submodule operate?
    How to interconnect them?
  If necessary, you should add a diagram to your report.
    Handwritten diagram is OK.

## Slide 11: Report
Implementation
  You should explain your Verilog code. For example:
    The overall structure of your implementation
    A short, but meaningful description for each of your non-trivial modules
    The interactions between modules when they run a given scenario
  Do NOT explain too much details of your implementation.
  Do NOT show the waveform results.
    I will check your waveform results during the demo.

## Slide 12: Report
Discussion
  You can write anything valuable that you want to inform. For example:
    Important decisions you made
    Difficulties in designing and implementing, and your solutions for these
    Differences between your design and implementation, and the reasons for these
    Feedback to TAs
Conclusion
  You don’t need to repeat the contents of the Introduction section.
  You just need to answer the following question:
    Did you succeed in achieving the goals described in the Introduction section?
      If not, which goals could not be achieved? Why?

## Slide 13: Demo
You will be asked to
Show the TA that your implementation works
  We will provide a testbench code for testing your implementation.
Answer some questions about your design and implementation
  If you did your assignment well, you don’t have to worry!