## Slide 1: Introduction to Verilog
Sanghwan Jang
Original slides created by Gwangmu Lee
CSED311 Computer Architecture

## Slide 2: HDL & Verilog

## Slide 3: HDL: Hardware Description Language
Programming language for programmable chips
input A, B;
output Q;
assign Q = A & B;
FPGA
Code written in HDL
Synthesis

## Slide 4: HDL: Hardware Description Language
Programming language for programmable chips
input A, B;
output Q;
assign Q = A & B;
FPGA
Code written in HDL
Synthesis
Examples of HDL: Verilog, VHDL, …
We will use Verilog!

## Slide 5: ModelSim
Tool for Verilog programming
How to install and use?
  Refer to Lab0_ModelSim.pdf file! (LMS)

## Slide 6: Verilog Example

## Slide 7
`timescale 1ns / 100ps
module AND (
input [3:0] A,
input [3:0] B,
output [3:0] Q);
reg [3:0] Q;
always begin
Q = A & B;
end
endmodule
Let’s start with this!
(bitwise AND module)

## Slide 8
`timescale 1ns / 100ps
module AND (
input [3:0] A,
input [3:0] B,
output [3:0] Q);
reg [3:0] Q;
always begin
Q = A & B;
end
endmodule
1ns: Unit of Delay
100ps: Unit of Simulation

## Slide 9
`timescale 1ns / 100ps
module AND (
input [3:0] A,
input [3:0] B,
output [3:0] Q);
reg [3:0] Q;
always begin
Q = A & B;
end
endmodule
Start of Module
Module
  Chip or Component of Chip
  Interface + Behavior Interface: Input & Output Behavior: Function
  Similar to OOP Class

## Slide 10
`timescale 1ns / 100ps
module AND (
input [3:0] A,
input [3:0] B,
output [3:0] Q);
reg [3:0] Q;
always begin
Q = A & B;
end
endmodule
Declaration of Input & Output
Input & Output (called Ports)
[3:0]: Declaration of Bit Range
  4-bits (3 to 0)
  Why not [0:3]? Explained later…

## Slide 11
`timescale 1ns / 100ps
module AND (
input [3:0] A,
input [3:0] B,
output [3:0] Q);
reg [3:0] Q;
always begin
Q = A & B;
end
endmodule
Declare Output Q as Register
A
B
Q
Module AND
reg Q

## Slide 12
`timescale 1ns / 100ps
module AND (
input [3:0] A,
input [3:0] B,
output [3:0] Q);
reg [3:0] Q;
always begin
Q = A & B;
end
endmodule
Always Executed
if any of the Inputs are changed

## Slide 13
`timescale 1ns / 100ps
module AND (
input [3:0] A,
input [3:0] B,
output [3:0] Q);
reg [3:0] Q;
always begin
Q = A & B;
end
endmodule
Assign A & B to Register Q

## Slide 14
`timescale 1ns / 100ps
module AND (
input [3:0] A,
input [3:0] B,
output [3:0] Q);
reg [3:0] Q;
always begin
Q = A & B;
end
endmodule
End of Module

## Slide 15: Verilog Syntax

## Slide 16: Timescale
Declare time units needed for source code simulation
  Typically inserted at the very beginning of the code.
  `timescale <Unit of Delay> / <Unit of Simulation>
Unit of Delay
  Ex) #100; // delay for 100 * 1ns
Unit of Simulation
  Time resolution of simulation
`timescale 1ns / 100ps

## Slide 17: Module
Corresponds to a chip or a component of a chip
Interface + Design Behavior
  Interface: Input and Output. Passage through which values pass. (Port)
  Design Behavior:
  What output will be given for the input?
  How will the internal state change?
Similar to Class in Object-Oriented Programming
module AND (input A, input B, output Q);
assign Q = A & B;
endmodule
Module Port
Module Body

## Slide 18: Module
module AND (input A, input B, output Q);
assign Q = A & B;
endmodule
module AND_test ();
reg X, Y; wire W;
AND aaa (X, Y, W);
endmodule
Instantiation
reg X
reg Y
module AND
A
B
Q
wire W
module AND_test

## Slide 19: Port
Collectively refers to the Input and Output of the Module.
Basically declared as wire(Wire).
  Optionally can be declared as reg(Register).
Only wire-wire and reg-wire connections are possible
  Reg-reg connection is impossible.
module always_one (output Q);
reg Q;
initial Q = 1;
endmodule
Declare Output Q as reg

## Slide 20: Data Type
wire (Wire)
  Wire, Define physical connections
reg (Register)
  1-bit D flip-flop. (1-bit Register)
  Can assign values during simulation.
Can be represented as an Bit Vector
  ex) wire [0:31] addr; // Big-endian reg [31:0] eax; // Little-endian (Recommended)

## Slide 21: Data Type
Value Reference
  ex) addr // all bits of addr addr[0] // 0th bit of addr addr[3:0] // 3~0th bits of addr
Value Concatenation
  ex) { eax[0], eax[31:1] } // 0th bit of eax + 31~1st bit of eax
31th ~ 1st Bits
0th
eax
0th
31th ~ 1st Bits
{ eax[0], eax[31:1] }

## Slide 22: Bit-vector is the only data type in Verilog
A bit can take on one of four values
An X bit might be a 0, 1, Z, or in transition. We can set bits to be X in situations where we don’t care what the value is. This can help catch bugs and improve synthesis quality.
Value | Meaning
0 | Logic Zero
1 | Logic One
X | Unknown Logic Value
Z | High Impedance, Floating

## Slide 23: Verilog 문법: Module Body
Verilog Syntax: Module Body

## Slide 24: Structured Procedure
module AND (input A, input B, output Q);
reg Q; wire AnB;
assign AnB = A & B;
always begin
Q = AnB;
end
endmodule
Structured Procedure
A type of code block.
  always: Always running block without condition
  Initial: Block that executes only once during module instantiation

## Slide 25: Initial Procedure
Runs only once during module instantiation.
Can contain multiple statements using begin and end.
initial begin
clk = 0;
x = 1;
end
initial clk = 0;
initial x = 1;

## Slide 26: Always Procedure
(When certain conditions are met) always called.
If there is no condition, called infinitely.
reg clk;
initial clk = 0;
always begin
#50;
clk = ~clk;
end
clk value is assigned as 0
clk value changed
Always block is called
After a delay of 50 (Important!)
 clk value reversed

## Slide 27: Other Procedure
Function, Task
  Similar to function in C
  Used to define a sub-module within a module.
  (You don’t need to use it,
  but if you are interested, study it yourself!)

## Slide 28: Verilog 문법: Assignments
Verilog Syntax: Assignments

## Slide 29: Assignments
module AND (input A, input B, output Q);
reg Q; wire AnB;
assign AnB = A & B;
always begin
Q = AnB;
end
endmodule
Continuous Assignments
Procedural Assignments
Used to assign wire connection or value.
  Continuous: Define wire connection
  Procedural: (In procedure) Store value in reg
Revisiting AND example..

## Slide 30: Continuous Assignments
Used to assign a wire connection to a wire
  ex) wire a, b, c; assign c = a & b; // wire c is defined as a & b.
  It is generally used outside procedure.
Can be used in conjunction with wire declaration.
  ex) wire a, b; wire c = a & b;
Once assigned, it cannot be changed during simulation.

## Slide 31: Continuous Assignments
You can give delay to assignment itself.
  ex) wire a, b, c; assign #10 c = a & b; // a & b is assigned to c after a delay of 10.
  Can be used to model the delay in wire connections.
Can be treated like an alias. (Remind reference type in C++)
  ex) wire a, b; assign b = a; // b is exactly the same as a

## Slide 32: Procedural Assignments
(In procedure) Used to store value in reg.
  ex)
Delay Modeling
  ex) #10 clk = 0; // assign 0 to clk after a delay of 10 #10 clk = #20 tmp; // load tmp after a delay of 20, and // store it to clk after a delay of 10
reg clk;
initial begin
clk = 0;
end

## Slide 33: Types of Procedural Assns.
Blocking Assignments
  Execute assignments according to statement order.
  Use ‘=‘ operator.
  The order between procedures(code blocks) is also valid.
reg a, b;
initial begin
a = 0;
b = 1;
end
reg a, b;
initial begin
a = 0;
end
Initial begin
b = 1;
end
In both cases a = 0 is executed first,
and then b = 1 is executed.

## Slide 34: Types of Procedural Assns.
Non-blocking Assignments
  Execute assignments simultaneously without any order.
  Use ‘<=’ operator.
reg a, b;
initial begin
a <= 0;
b <= 1;
end
reg a, b;
initial begin
b <= 1;
a <= 0;
end
In both cases, a <= 0 and b <= 1
are executed simultaneously.

## Slide 35: Blocking vs. Non-blocking
reg a, b, c;
initial begin
#50;
b = a;
c = b;
end
reg a, b, c;
initial begin
#50;
b <= a;
c <= b;
end
Blocking
Assn.
Non-blocking
Assn.
* Initially, a = 0 and b = 1
Cycle | a | b | c
0 | 0 | 1 | 
50 | 0 | 0 | 0
Cycle | a | b | c
0 | 0 | 1 | 
50 | 0 | 0 | 1

## Slide 36: Mixed Blocking
Don’t even think about it!
There is no syntax problem, but the results are hard to predict.
Use non-blocking assignment mostly.
  It is closer to real hardware.

## Slide 37: Verilog 문법: Delay & Event
Verilog Syntax: Delay & Event

## Slide 38: Delay
Used when delaying module behavior during simulation.
  ex) #100; // Wait for a delay of 100
Used for more realistic hardware modeling
  Can even give a random value instead of a fixed value.
  Not to be used to “debug” your Verilog design!!
We limit the use of delay to two parts in Lab assignments.
  Clock (Code to generate the signal)
  Testbench (Code to test the module)

## Slide 39: Delay
In begin … end, delay is cumulatively applied.
initial begin
#50 clk = 0;
#50 x = 1;
end
initial #50 clk = 0;
initial #100 x = 1;

## Slide 40: Event
Used to give execution condition of specific procedure block or procedural assignment.
module dummy (input a,
output b);
reg b;
event e;
initial begin
#50;
-> e;
end
Wait for a delay of 50,
and raise event e.
Always execute when event e occurs
always @e begin
b <= 1;
end
endmodule

## Slide 41: Event
Used to give execution condition of specific procedure block or procedural assignment.
module dummy (input a,
output b);
reg b;
event e;
initial begin
#50;
-> e;
end
Wait for a delay of 50,
and raise event e.
Always execute when event e occurs
always @e begin
b <= 1;
end
endmodule
If an event condition is given,
execute only when this condition is met

## Slide 42: Event
All data(wire or reg) changes can be used as events.
  ex) reg a; always @(a) begin… // execute when the value of ‘reg a’ changes
Change of a value can be used as an event.
  ex) reg a; always @(posedge a) begin // when ‘reg a’ switches from 0 to 1 always @(negedge a) begin // when ‘reg a’ switches from 1 to 0
Or-ing between events are allowed
  ex) always @(a or b) begin..

## Slide 43: Event
Can be used within a procedure block or statement.
reg clk, a, b;
initial begin
@(posedge clk) a <= 0;
@(posedge clk) b <= 1;
end
Initially, wait until clk changes 0 → 1 and then execute.
Next, wait until clk changes 0 → 1 and then execute.

## Slide 44: Verilog 문법: Flow Control
Verilog Syntax: Flow Control

## Slide 45: Flow Control
Used only within a structured procedure.
Syntax provided for ease of implementation.
  It is far from real hardware implementation.
Types
  If Statement
  Case Statement
  Loop Statement

## Slide 46: If Statement
Conditionally executes statements.
Can also be expressed with the “?” operator from C (implemented as a mux)
initial begin
if (a == 5) begin
b <= 15;
end
else begin
b <= 25;
end
end
wire c = (a == 5) ? 15 : 25;
initial begin
b <= c;
end

## Slide 47: Case Statement
Optionally executes statements based on the value.
initial begin
case (a)
5 : b <= 15;
default : b <= 25;
endcase
end
initial begin
if (a == 5) begin
b <= 15;
end
else begin
b <= 25;
end
end

## Slide 48: Loop Statement
Repeat
  Repeat the statement for the specified number of times.
initial begin
repeat (4) c = c + 1;
end
initial begin
c = c + 1;
c = c + 1;
c = c + 1;
c = c + 1;
end

## Slide 49: Loop Statement
Forever
  Repeat the statement indefinitely.
initial begin
forever #5 c = c + 1;
end
initial begin
#5 c = c + 1;
#5 c = c + 1;
#5 c = c + 1;
#5 c = c + 1;
…
// repeated indefinitely
end

## Slide 50: Loop Statement
While, For
  Easy to use, but often impossible to implement with hardware.
  Can be used without problems when initializing array.
reg c;
initial begin
while (c < 10)
c = c + 1;
end
reg c;
initial begin
for (c = 0; c < 10; c = c + 1)
// Statement
end

## Slide 51: Verilog 문법: 기타
Verilog Syntax: Etc.

## Slide 52: Other General Syntax
Comment
  // or /* */ (similar to C)
Constant
  Format: <Number of Bits>’<Base><Value> <Base>  h(Base 16), d(Base 10), o(Base 8), b(Base 2) <Value>  0~9, A~F, X(Unknown Value), Z(High Impedance)
  ex) 8’b01001111 (8-bit Binary 01001111) 16’hAF (16-bit Hexadecimal AF)
  Decimal numbers can be entered without any special format.

## Slide 53: Other General Syntax
Operators
  Basically similar to C operators (But no ++ & --)
  Unary/Binary Logical Operators and(&), nand(~&), or(|), nor(~|), xor(^), xnor(^~ or ~^), negation(~)
  Equal Operators a == b, a != b : return X if a or b contains X or Z a === b, a !== b : even compares X and Z

## Slide 54: Reference
Verilog References
  Verilog Tutorial & Examples http://www.asic-world.com/verilog/index.html
  Verilog Syntax: Compact Summary https://www.csee.umbc.edu/portal/help/VHDL/verilog/summary.html

## Slide 55
>> Thank You!